## Slide 1: Schematic Design
Altium Designer has been used!
No galvanic isolation is needed!
Some extra components are used which are not discussed in component selection part!

## Slide 2: Schematic Design
IntVCC Pin: To maintain internal VCC, datasheet recommends minimum 2.2uF ceramic capacitor. 4.7uF capacitor is used.
Bias Pin: This pin takes internal supply from output, 4.7uF ceramic capacitor is recommended.
Smode Pin: For standby operation, grounded for normal operation.

## Slide 3: Schematic Design
VC Pin: For loop compensation. Datasheet recommends an R-C network to stabilize the operation generally with 20kohm and 220nF. However demo board uses 10kohm and 100nF, and when we compare these two, 10kohm and 100nF R-C networks gives better transient response.
IREG/SS Pin: For output current regulation. The formula in the datasheet gives us a 50kohm resistor to regulate output current at 8.33A.
TC Pin: For temperature compensation, experimentally adjusted. We have taken demo board value 121kohm and connected to FB pin.

## Slide 4: Schematic Design
We have used inut bypass capacitors to eliminate any possible high frequency noises.
We have used 20 ohm MOSFET gate resistor to limit dI/dt in the gate, for safe switching.
We have used 10kohm gate pull-down resistor for safety.

## Slide 6: PCB Design
Rules and Validations
According to IPC2221B, 0-15V clearance should be minimum 0.1mm
300-500V should be minimum 2.5mm for bare PCB, 0.8mm for coated PCB

## Slide 7: PCB Design
Input Minimum Line Width: 1.3mm (6.5A)
(5A Max.)
Input Minimum Via hole: 0.3mm (3.78A)
Via’s are used as pairs!

## Slide 8: PCB Design
Design Rule Check

## Slide 9: 2D Design
Two isolated sides (Left: Input, Right:Output)
0.4mm spacing with board borders
Positive and negative terminal markings for safety! (Protection Circuit Bonus)

## Slide 10: 2D Design
According to IPC2221B, 4.7mm isolation is capable up to 940V in bare PCB and 1750V in coated PCB
We have designed for coated PCB!

## Slide 11: 2D Design

## Slide 12: 2D Design

## Slide 13: 2D Design

## Slide 14: 2D Design

## Slide 15: 2D Design
Dimensions
  33mm x 54.6mm

## Slide 16: 3D Design
3D Models are placed
Compact and Industrial Product!
Top Layer

## Slide 17: 3D Design
Bottom Layer:

## Slide 18: 3D Design
Side View:

## Slide 19: 3D Design

## Slide 20: 3D Design

## Slide 21: 3D Design
PCB Material Selection:
  18um Base Copper + 18um Plating Thickness (1 oz Copper)
  FR-4 Material (low conduction loss compared to Aluminum)
  1.6mm Card Thickness

## Slide 22: 3D Design
Dimesions:
  Top Layer Highest Component: 20.25mm (Transformer)
  Bottom Layer Highest Component: 3.2mm (Output Diode)
  Card Thickness: 1.6mm
  Total: 23.05mm z-axis  Dimensions: 54.6mm x 33mm x 23.05mm Volume: 41531.49 mm3
  Box is designed with margins: 64mm x 40mm x 30mm Volume: 76800 mm3 (Industrial Design Bonus)

## Slide 23: Box Design
Box has screw holes for fiducials
There are 6 opening at bottom side for airflow to output diodes
Box cover is connected with metric 1.5 screws

## Slide 24: Box Design
Bottom View
Input View
Output View

## Slide 25: Box Design
Box with Cover

## Slide 26: Hardware Design Conclusion
Design Rules
Line-Via Currents
Components
Isolation Boundary
Card Material
Copper Thickness

## Slide 27: Cost Analysis
Component Price: 9.78$
PCB Price: 0.197$
Litz Wire: 3.9$
Total Cost for one PCB: 13.88$ (Cheapest Design Bonus)

## Slide 28: Martian Power Solutions
Enhanced Simulation
Enhanced Magnetic Design
Power Loss and Thermal Calculations
Hardware Design
Cost Analysis

## Slide 29: Thank You!
SPOILER ALERT!